## Slide 1: Cavity Pressure Acceleration in laser-induced, mixed-fuel fusion reactions
Przemysław Tchórz1*, Tomasz Chodukowski1, Stefan Borodziuk1, Marcin Rosinski1, Mattia Cipriani2, Zofia Rusiniak1, Roman Dudzak3,4, Michal Krupka3,4,5, Jakub Cikhardt4,6, Tomas Burian3, Sushil Singh3,4, Maciej Szymanski1, Anna Marchenko1,7, Michal Kustosz1, Shubham Agarwal3,8, Josef Krasa3, Robert Swierczynski9, Janina Pokorska1, Tadeusz Pisarczyk1, Daniel Klir6, Jiri Skala3,4, Jan Dostal3,4, Miroslav Krus4 and Libor Juha3
Przemysław Tchórz (IPPLM)
5th International Workshop on Proton-Boron Fusion, Belgrade, 08.09.2025 – 11.09.2025
1 Institute of Plasma Physics and Laser Microfusion, Poland
2 ENEA, Fusion and Technologies for Nuclear Safety Department, Italy
3 Institute of Physics, AS CR, Prague, Czech Republic
4 Institute of Plasma Physics, AS CR, Czech Republic
5 Faculty of Nuclear Sciences and Physical Engineering, Czech Technical University in Prague, Czech Republic
6 Faculty of Electrical Engineering, Czech Technical University in Prague, Czech Republic
7 National Science Center, Kharkiv Institute of Physics and Technology, Ukraine
8 Faculty of Mathematics and Physics, Charles University in Prague, Prague, Czech Republic
9 Military University of Technology, Poland

## Slide 2
Outline
Introduction
  Cavity Pressure Acceleration – overview
  Latest experimental results – products of DD reaction by means of CPA method on PALS laser system (Prague, Czech Republic)
Simulations – proton boron reaction using CPA proton beam and optimization of cavity design for DD reaction with kJ, ns-class laser pulses
  MC simulations of proton boron reaction basing on experimental results
  Radiative-hydrodynamic simulations – PALS experiment
  Radiative-hydrodynamic simulations – upcoming experiment at ELI Beamlines
Experimental design - proton-boron fusion in pitcher-catcher configuration at ELI Beamlines L4n laser system

## Slide 3
Cavity Pressure Acceleration – overview
Przemysław Tchórz (IPPLM) 5th International Workshop on Proton-Boron Fusion, Belgrade, 08.09.2025 – 11.09.2025

## Slide 4
1. Introduction: Cavity Pressure Acceleration – overview
Przemysław Tchórz (IPPLM) 5th International Workshop on Proton-Boron Fusion, Belgrade, 08.09.2025 – 11.09.2025
Historically, Cavity Pressure Acceleration (CPA) was proposed as an alternative driver for direct-drive Impact Fast Ignition (Murakami et al 2005 Plasma Phys. Control. Fusion 47 B815).
Borodziuk et al. Appl. Phys. Lett. 95, 231501 (2009)
Borodziuk et al. Appl. Phys. Lett. 99, 231501 (2011)
Borodziuk et al. Appl. Phys. Lett. 93, 101502 (2008)
for both 10um Al () and 20um PS () foils
At that time, the highest velocity obtained at NRL, accelerating 10.5um CH flyers to , meeting the velocity criteria for Impact Fast Ignition, however underperforming when it came to the density of the impactor.
Murakami et al 2005 Plasma Phys. Control. Fusion 47 B815
Requirements for the ablated impactor shell:

## Slide 5
1. Introduction: Cavity Pressure Acceleration – overview
Przemysław Tchórz (IPPLM) 5th International Workshop on Proton-Boron Fusion, Belgrade, 08.09.2025 – 11.09.2025
Historically, Cavity Pressure Acceleration (CPA) was proposed as an alternative driver for direct-drive Impact Fast Ignition (Murakami et al 2005 Plasma Phys. Control. Fusion 47 B815).
Borodziuk et al. Appl. Phys. Lett. 93, 101502 (2008)
Up to for 500um Al foils () obtained using 250ps, 190J laser pulse (
Borodziuk et al. Appl. Phys. Lett. 95, 231501 (2009)
Borodziuk et al. Appl. Phys. Lett. 99, 231501 (2011)
Borodziuk et al. Appl. Phys. Lett. 93, 101502 (2008)
for both 10um Al () and 20um PS () foils
At that time, the highest velocity obtained at NRL, accelerating 10.5um CH flyers to , meeting the velocity criteria for Impact Fast Ignition, however underperforming when it came to the density of the impactor.

## Slide 6
1. Introduction: Cavity Pressure Acceleration – overview
Chodukowski et al. AIP Advances 10, 085206 (2020)
In 2020, roughly 10 years after last experimental activities regarding CPA scheme, the idea was revisited with slightly different setup. Instead of metallic flyers, deuterated polyethylene was used.
for foil, while producing neutrons per shot
DD reaction has two possible channels:
(50%)
(50%)
Przemysław Tchórz (IPPLM) 5th International Workshop on Proton-Boron Fusion, Belgrade, 08.09.2025 – 11.09.2025

## Slide 7
Latest experimental results – products of DD reaction by means of CPA method on PALS laser system (Prague, Czech Republic)

## Slide 8
Introduction: Latest experimental results – products of DD reaction by means of CPA method on PALS laser system
(Prague, Czech Republic)
Tchórz et al. Phys. Plasmas 31, 084503 (2024)
Additional acceleration occurs, which causes the DD protons to gain additional energy, up to 5.2 MeV. In several shots (example: green spectrum), strong peak around 3.7 MeV visible, but at lower maximum energy: the additional accelerating force was weaker.
Most likely, the additional accelerating force is attributed to strong electrical fields arising inside the cavity – has to be investigated in following experimental campaigns.
30⁰ in respect to the target normal

## Slide 9
CR 39 detector measurements 50 cm away from target, 30 deg (under TPS line of sight) – below 65𝜇𝑚 filter thickness strong saturation
Thickness [] | Cut-off Energy [MeV]
20 | 1.75
50 | 2.25
65 | 2.65
83 | 3
 | Cut-off Energy [MeV]
20 | 1.75
50 | 2.25
65 | 2.65
83 | 3
Introduction: Latest experimental results – products of DD reaction by means of CPA method on PALS laser system
(Prague, Czech Republic)

## Slide 10
Obtained number of particles for energies approximately 3 MeV, which corresponds well with TPS results
Thickness [] | Cut-off Energy [MeV]
20 | 1.75
50 | 2.25
65 | 2.65
83 | 3
 | Cut-off Energy [MeV]
20 | 1.75
50 | 2.25
65 | 2.65
83 | 3
Introduction: Latest experimental results – products of DD reaction by means of CPA method on PALS laser system
(Prague, Czech Republic)

## Slide 11
Introduction: Latest experimental results – products of DD reaction by means of CPA method on PALS laser system
(Prague, Czech Republic)
Chodukowski, T., Borodziuk, S., Tchórz, P. et al. Sci Rep 15, 21863 (2025).
80% of neutrons are produced before density peak leaves cavity channel, which means that the mechanism behind neutron production is not a beam-target type
Using powdered fuel instead of flyer-ablator geometry should give similar neutron yield with much simpler construction
1D simulation – custom code (Jach et al. Computer Modelling of Dynamic Interaction of Bodies by Free Particle (PWN Method, 2001) (in polish)

## Slide 12
Introduction: Latest experimental results – products of DD reaction by means of CPA method on PALS laser system
(Prague, Czech Republic)
# | Laser energy | Laser intensity | Neutron yield | Neutron yield
 | [J] | [] | (a) | (b)
57548 | 721 |  |  | 
57554 | 714 |  |  | 
59102 | 581 |  |  | n/a
59104 | 563 |  |  | n/a
59117 | 592 |  |  | n/a
59125 | 563 |  |  | n/a
# | Laser energy | Laser intensity | Neutron yield | Neutron yield
 | [J] |  | (a) | (b)
57548 | 721 |  |  | 
57554 | 714 |  |  | 
59102 | 581 |  |  | n/a
59104 | 563 |  |  | n/a
59117 | 592 |  |  | n/a
59125 | 563 |  |  | n/a
Chodukowski, Borodziuk, Tchórz et al. Sci Rep 15, 21863 (2025).
Notes: Neutron production independent from used geometry

## Slide 13
Introduction: Latest experimental results – products of DD reaction by means of CPA method on PALS laser system
(Prague, Czech Republic)
Chodukowski, T., Borodziuk, S., Tchórz, P. et al. Sci Rep 15, 21863 (2025).

## Slide 14
Simulations – proton boron reaction using CPA proton beam and optimization of cavity design for DD reaction with kJ, ns-class laser pulses

## Slide 15
2. Simulations: MC simulations of proton boron reaction basing on experimental results
Monte Carlo simulations using FLUKA code (INFN, ver. FLUKA 2023.3.4)
Experimentally measured proton energy spectrum used as input
Most optimal thickness:
Increase of neutron production from secondary reactions with the target thickness
For more neutrons are generated than alphas emitted from target

## Slide 16
2. Simulations: MC simulations of proton boron reaction basing on experimental results
Monte Carlo simulations using FLUKA code (INFN, ver. FLUKA 2023.3.4)
Experimentally measured proton energy spectrum used as input
Notes: Secondary reactions:
11B(p,n)11C,
11B(p,n)14N ->>>>> 14N(alpha,n)17F

## Slide 17
2. Simulations: Radiative-hydrodynamic simulations – PALS experiment
350ps FWHM, 600J, (PALS) Simulation length: 10 ns, 100ps step

## Slide 18
2. Simulations: Radiative-hydrodynamic simulations – PALS experiment
Cavity used during PALS experiment was too wide, resulting in low efficiency of heating and pressurizing the plasma, yet still allowed sufficient for DD reaction

## Slide 19
2. Simulations: Radiative-hydrodynamic simulations – upcoming experiment at ELI Beamlines
1ns FWHM, 300J, (ELI Beamlines L4n ATON laser) Simulation length: 3 ns, 100ps step
Flat CD and cavity:

## Slide 20
2. Simulations: Radiative-hydrodynamic simulations – upcoming experiment at ELI Beamlines
1ns FWHM, 300J, (ELI Beamlines L4n ATON laser) Simulation length: 3 ns, 100ps step
Flat CD and cavity:

## Slide 21
2. Simulations: Radiative-hydrodynamic simulations – upcoming experiment at ELI Beamlines
Density – 100x higher comparing to flat target, 10x comparing to PALS (at exit)
Electron temperature – similar level to max from PALS, but for longer duration
Pressure – 20x higher during plasma release time
Notes: Order of magnitude lower laser intensity : ELI vs PALS, still comparable temperatures obtainable

## Slide 22
Experimental design - proton-boron fusion in pitcher-catcher configuration at ELI Beamlines L4n laser system

## Slide 23
3. Experimental design - proton-boron fusion in pitcher-catcher configuration at ELI Beamlines L4n laser system
Cavity Pressure Acceleration in pitcher-catcher-based proton-boron experiment
L4n laser system:
focal spot diameter
Simplified design adapted to higher repetition of shots, optimized according to FLASH simulations for highest values of

## Slide 24
3. Experimental design - proton-boron fusion in pitcher-catcher configuration at ELI Beamlines L4n laser system
New kind of fuel - nano-particle „foam” ppC:H/D of desired thickness
(Tosca et al. Materials Today Sustainability 30 (2025))
Cavity Pressure Acceleration in pitcher-catcher-based proton-boron experiment
L4n laser system:
focal spot diameter

## Slide 25
3. Experimental design - proton-boron fusion in pitcher-catcher configuration at ELI Beamlines L4n laser system
New kind of catcher materials – e.g „fiber cloth” suitable for high-rep experiments
Cavity Pressure Acceleration in pitcher-catcher-based proton-boron experiment
L4n laser system:
focal spot diameter

## Slide 26
3. Experimental design - proton-boron fusion in pitcher-catcher configuration at ELI Beamlines L4n laser system
L4n laser system:
focal spot diameter
New materials:
Thin boron catchers (down to ): 64,1% H3BO3 + 20,8% ethylenamine
Deuterated ammonia-borane: BD₆N
Additional diagnostics:
Electron spectrometer
Second TPS unit
Neutron time-of-flight
Advanced ion time-of-flight detectors
HPGe
X-ray detectors

## Slide 27
3. Experimental design - proton-boron fusion in pitcher-catcher configuration at ELI Beamlines L4n laser system
L4n laser system:
focal spot diameter
New materials:
Thin boron catchers (down to ): 64,1% H3BO3 + 20,8% ethylenamine
Deuterated ammonia-borane: BD₆N
Additional diagnostics:
Electron spectrometer
Second TPS unit
Neutron time-of-flight
Advanced ion time-of-flight detectors
HPGe
X-ray detectors

## Slide 28
3. Experimental design - proton-boron fusion in pitcher-catcher configuration at ELI Beamlines L4n laser system
talks of:
M. Manojlovic
G. Lastovicka-Medin
L4n laser system:
focal spot diameter
Additional diagnostics:
Electron spectrometer
Second TPS unit
Neutron time-of-flight
Advanced ion time-of-flight detectors
HPGe
X-ray detectors
New materials:
Thin boron catchers (down to ): 64,1% H3BO3 + 20,8% ethylenamine
Deuterated ammonia-borane: BD₆N
Notes: Deuterated ammonia borane – potentially more deuterium fuel than CD2

## Slide 29
Thank you!
This work has been carried out within the framework of the EUROfusion Consortium, funded by the European Union via the Euratom Research and Training Program (Grant Agreement No. 101052200—EUROfusion). Views and opinions expressed are, however, those of the author(s) only and do not necessarily reflect those of the European Union or the European Commission. Neither the European Union nor the European Commission can be held responsible for them.
This scientific paper has been published as part of the international project called “PMW,” co-financed by the Polish Ministry of Science and Higher Education within the framework of the scientific financial resources for 2020 – 2022 under the Contract No. 5199/PALS/2021/0 and was partially funded by LASERLAB-EUROPE (Grant No. PALS002750). This research work was supported by the Ministry of Science and Higher
Education as part of the IPPLM statutory subsidy. This research work was supported by the Ministry of Youth and Sports of the Czech Republic (Project x Nos. LM2023068 and LM2018114 (PALS RI). This work was supported as well from the Czech Academy of Science’s project “Strategy AV21—Light at the service of society.”
The dissertation is based upon work from COST Action CA21128 “PROton BOron Nuclear fusion: from energy production to medical applications,” supported by COST (European Cooperation in Science and Technology —
www.cost.eu). The computing resources and the related technical support used for this work have been provided by CRESCO/ENEAGRID High Performance Computing infrastructure and its staff. CRESCO/ENEAGRID High Performance Computing infrastructure is funded by ENEA, the Italian National Agency for New Technologies, Energy and Sustainable Economic Development and by Italian and European research programmes.

## Slide 30
Extra slide